| KEY to AERODROME FORECAST (TAF) and AVIATION ROUTINE WEATHER REPORT (METAR) |
| --- |
| TAF KPIT 091730Z 091818 15005KT 5SM HZ FEW020 WS010/31022KT FM1930 30015G25KT 3SM SHRA OVC015 TEMPO 2022 1/2SM +TSRA OVC008CB FM0100 27008KT 5SM SHRA BKN020 0VC040 PROB40 0407 1SM -RA BR FM1015 18005KT 6SM -SHRA OVC020 BECMG 1315 P6SM NSW SKC METAR KPIT 091955Z COR 22015G25KT 3/4SM R28L/2600FT TSRA OVC010CB 18/16 A2992 RMK SLP045 T01820159 |
| Forecast | Explanation | Report |
| TAF | Message type: TAF-routine or TAF AMD-amended forecast, METAR-hourly, SPECI-special or TESTM-non-commissioned ASOS report | METAR |
| KPIT | ICAO location indicator | KPIT |
| 091730Z | Issuance time: ALL times in UTC "Z", 2-digit date, 4-digit time | 091955Z |
| 091818 | Valid period: 2-digit date, 2-digit beginning, 2-digit ending times |  |
|  | In U.S. METAR: CORrected ob; or AUTOmated ob for automated report with no human intervention; omitted when observer logs on | COR |
| 15005KT | Wind: 3 digit true-north direction, nearest 10 degrees (or VaRiaBle); next 2-3 digits for speed and unit, KT (KMH or MPS); as needed, Gust and maximum speed; 00000KT for calm; for METAR, if direction varies 60 degrees or more, Variability appended, e.g. 180V260 | 22015G25KT |
| 5SM | Prevailing visibility: in U.S., Statute Miles & fractions; above 6 miles in TAF Plus6SM. (Or, 4-digit minimum visibility in meters and as required, lowest value with direction) | 3/4SM |
|  | Runway Visual Range: R; 2-digit runway designator Left, Center, or Right as needed; "/"; Minus or Plus in U.S, 4-digit value, FeeT in U.S. (usually meters elsewhere); 4-digit value Varialbility 4-digit value (and tendency Down, Up or No change) | R28L/2600FT |
| HZ | Significant present, forecast and recent weather: see table (below) | TSRA |
| FEW020 | Cloud amount, height and type: SKy Clear 0/8, FEW >0/8-2/8, SCaTtered 3/8-4/8, BroKeN 5/8-7/8, OVerCast 8/8; 3-digit height in hundreds of ft; Towering CUmulus or CumulonimBus in METAR; in TAF, only CB. Vertical Visibility for obscured sky and height "VV004". More than 1 layer may be reported or forecast. In automated METAR reports only, CLeaR for "clear below 12,000 feet" | OVC010CB |
|  | Temperature: degrees Celsius; first 2 digits, temperature "/" last 2 digits, dew-point temperature; Minus for below zero, e.g., M06 | 18/16 |
|  | Altimeter setting: indicator and 4 digits; in U.S., A-inches and hundredths; (Q-hectoPascals, e.g. Q1013) | A2992 |
| WS010/31022KT | In U.S. TAF, non-convective low-level (<=2,000 ft)Wind Shear; 3-digit height (hundreds of ft); "/", 3-digit wind direction and 2-3 digit wind speed above the indicated height, and unit, KT |  |
|  | In METAR, ReMarK indicator & remarks. For example:Sea-Level Pressure in hectoPascals & tenths, as shown: 1004.5 hPa; Temp/dew-point in tenths °C, as shown: temp 18.2°C, dew-point 15.9°C | RMK SLP045 T01820159 |
| FM1930 | FroM and 2-digit hour and 2-digit minute beginning time: indicates significant change. Each FM starts on a new line, indented 5 spaces. |  |
| TEMPO 2022 | TEMPOrary: changes expected for < 1 hour and in total, < half of 2-digit hour beginning and 2-digit hour ending time period |  |
| PROB40 0407 | PROBability and 2-digit percent (30 or 40): probable condition during 2-digit hour beginning and 2-digit hour ending time period |  |
| BECMG 1315 | BECoMinG: change expected during 2-digit hour beginning and 2-digit hour ending time period |  |

Table of Significant Present, Forecast and Recent Weather - Grouped in categories and used in the order listed below; or as needed in TAF, No Significant Weather.

QUALIFIER

Intensity or Proximity

- Light              "no sign" Moderate   + Heavy

VC Vicinity: but not at aerodrome;

in U.S. METAR, between 5 and 10SM of the point(s) of observation;

in U.S. TAF, 5 to 10SM from center of runway complex

(elsewhere within 8000m)

Descriptor

MI Shallow           BC Patches           PR Partial          TS Thunderstorm

BL Blowing           SH Showers           DR Drifting         FZ Freezing

WEATHER PHENOMENA

Precipitation

DZ Drizzle           RA Rain              SN Snow             SG Snow grains

IC Ice crystals      PL Ice pellets       GR Hail             GS Small hail/snow pellets

UP Unknown precipitation in automated observations

Obscuration

BR Mist(>= 5/8SM)    FG Fog(< 5/8SM)      FU Smoke            VA Volcanic Ash

SA Sand              HZ Haze              PY Spray            DU Widespread dust

Other

SQ Squall            SS Sandstorm         DS Duststorm        PO Well developed

FC Funnel cloud      +FC tornado/waterspout                      dust/sand whirls

- Explanations in parentheses "( )" indicate different worldwide practices.

- Ceiling is not specified; defined as the lowest broken or overcast layer, or the vertical visibility.

- NWS TAFs exclude turbulence, icing & temperature forecasts; NWS METARs exclude trend fcsts

- Although not used in US, Ceiling And Visibility OK replaces visibility, weather and clouds if: visibility >=10km; no cloud below 5000 ft (1500m) or below the highest minimum sector altitude, whichever is greater and no CB; and no precipitation, TS, DS, SS, MIFG, DRDU, DRSA, or DRSN.